## Slide 1: EECS151/251A Discussion
Christopher Yarp
Jan. 25, 2019

## Slide 2: About me
5th Year Graduate Student
  Advisor: John Wawrzynek
Work in the Berkeley Wireless Research Center (BWRC)
Prior Projects: Implementing Radio Basebands (DSP) in FPGAs
Current Research: Design Methodologies & Tools for DSP

## Slide 3: My Job
To help you get the most of this course!
  Running the discussion session
  Running the FPGA lab sections
  Answering questions in office hours and on Piazza

## Slide 4: What to expect from discussion
Review of important concepts from past week’s lectures
Answer your questions!
More examples
Please give me feedback on what is helpful!

## Slide 5: Textbook Resources
I may, from time to time, reference content from the Weste, Harris book mentioned in lecture
  CMOS VLSI Design: A Circuits and Systems Perspective, 4th Ed.
The textbook is not required but does provide additional explanation and examples

## Slide 6: Trends in Digital Design
Scaling Laws

## Slide 7: Moore’s Law
Number of transistors per ASIC die doubles every 1-2 years
  Typically fueled by shrinking transistors to increase density
General view: Moore’s Law is coming to an end (or at least slowing)
  Harder to scale the size of transistors to increase transistor density
  Cost/transistor is not scaling as well as it used to
https://www.eetimes.com/document.asp?doc_id=1333109

## Slide 8: Other ways of increasing transistor count
If it is harder to scale transistor sizes, what can we do?
Increase the size of the die!
  Well … we could do this up to a point. Undesirable to make dies much larger
    Large dies = poor yield = higher cost
Put more dies in a package!
  AMD Threadripper (Released)
  Intel 48-Core Cascade Lake (Announced)
AMD Threadripper “De-lidded”
https://www.extremetech.com/computing/253248-amd-threadripper-delidded-multi-core-surprise-hood
Silicon Dies
Package (Opened)

## Slide 9: Dennard Scaling & Frequency Scaling
Dennard Scaling
Voltage can be reduced as transistors are physically scaled down in size
  Lower power
Capacitance also scaled down
  Lower power, higher speed
Keeps power density constant, linearly improves delay (Weste, Harris 256)
Frequency Scaling
Keep voltage constant as transistors are scaled (Weste, Harris 256)
  Delay quadratically decreases (YAY!!)
  Power density cubically increases (NO!!)
  Generally stopped around 3-4 GHz
    Encountered the “power wall” – cannot dissipate that much power

## Slide 10: What do these laws mean for performance?
Moore’s Law
  Performance may increase for a given chip area
    Relies on parallelism
  Why not 2x when doubling number of transistors?
    Limited opportunities for parallelism
    Overhead
  Does your 4 core processor work 2x as fast as your last 2 core processor?
Frequency Scaling:
  Performance did mostly scale with frequency
    A 1.6 GHz processor performed approx. 2x better than 800 MHz processor without any change to architecture!
  Don’t really see this today
Notes: Ask John. Is Moore’s law really dead (is it transistors per die or transistors per package)? How about Dennard Scaling? Frequency scaling definitely is because of the power wall. It seems like we are scaling down the nominal Vdd of chips as processes scale down (although this is anecdotal to me. It seems true recently if you trust wikichip).
Does gate capacitance still scale? FinFet? Traditional Denard scaling would suggest that we would see linear increases in clock frequency. However, we don’t. Are we keeping frequency the same and decreasing voltage more than what would be required by Dennard scaling?
How about Vt, is it still scaling??
We havn’t talked about leackage.
Also, when talking about delay, should I mention net capacitance and speed of light?

## Slide 11: Are transistors still scaling?
Yes
  32 nm several years ago
  14 nm today
  7 nm today
  5 nm planned
What are the effects?
  More complex than traditional Dennard Scaling
  Voltage appears to generally be decreasing
  Clock speed not really changing

## Slide 12: Design Space, Tradeoffs, and the “Pereto Optimal” Frontier
We often have competing objectives when designing hardware
  High performance
  Low power
  Low cost
We usually can’t get everything we want - we need to make some tradeoffs
The “Perato Optimal” frontier represents the edge of the tradeoff space
  Can’t to go beyond the “Perato Optimal” frontier

## Slide 13: Logic Design

## Slide 14: Combinational Logic
Logic where the outputs only depend on the current inputs
  Do not depend on any previous inputs
Can be expressed using a Truth Table
  Enumerate all possible inputs
  Define the outputs
A | B | Out
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 15: Proving Equivalence with Truth Tables (Exhaustive Proof)
You can prove 2 circuits are (or are not) equivalent by comparing their truth tables
  Useful for checking your work

## Slide 16: Proving (or Disproving) Equivalence with Truth Tables (Exhaustive Proof)
C | B | A | A&&B | (A&&B)¦¦C | Out
0 | 0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0 | 1
0 | 1 | 0 | 0 | 0 | 1
0 | 1 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1 | 0
1 | 1 | 0 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1 | 0
C | B | A | A&&B | !(A&&B) | !C | Out
0 | 0 | 0 | 0 | 1 | 1 | 1
0 | 0 | 1 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 1 | 1 | 1
0 | 1 | 1 | 1 | 0 | 1 | 0
1 | 0 | 0 | 0 | 1 | 0 | 0
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 1 | 0 | 0
1 | 1 | 1 | 1 | 0 | 0 | 0

## Slide 17: Registers (State Elements)
Combinational logic is great but what about making decisions based on past inputs?
We need a way to store information!
Registers (FlipFlops) act as a storage element
  Move the input to the output at a the 0 to 1 transition of a “load” line
    There is some delay doing this
  Hold the output until the next 0 to 1 transition of the “load” line
  The “load” line is typically connected to the clock (clk)
clk
Q
D
D
Q
clk
n
n
0
1
X
0
2
1
Time

## Slide 18: Register Transfer Level (RTL)
Can split your design into combinational logic blocks and state elements (sequential logic)
This abstraction covers all digital logic design
Does not cover every electronic circuit you could make
  Combinational loops are not allowed
    When one of the inputs to your combinational logic is the output
      Ex: inverter wired to itself
This abstraction helps us when using HDL languages like Verilog!
  Describe combinational sections
  Describe sequential (state) sections
D
Q
clk
Comb. Logic
Comb. Logic
You may even have feedback from registers!

## Slide 19: ASICs vs. FPGAs

## Slide 20: ASIC vs FPGAs
ASIC
FPGA
Flexibility in placing standard cells during design
Can place exactly the cells you need
Arrays of General Logic Resources
  Lookup Tables
  Registers
  Multiplexers
  Memory
  DSP Blocks
  Interconnect Network
Programming the FPGA configures these general resources to implement your HW design

## Slide 21: ASIC vs FPGAs
ASIC
No unused logic -> you placed exactly what you needed
Inflexible after manufacturing -> only configurability is what you designed in
Design iteration time: months - years
High Fixed Manufacturing Cost (NRE – Non Reoccurring Engineering)
  Designing and verifying
    Limited flexibility -> better get the right design
    Expensive to manufacture again -> avoid needing to fix things and manufacture again
  Mask production (used during manufacturing)
  Setting up the production line
Low Incremental Manufacturing Cost
  Once the design is done and the production line is set up, producing more chips is not very expensive
Better sell a lot of chips to amortize the NRE!
FPGA
Generality -> unused logic in some applications
Remains Flexible -> can change design later (reprogram FPGA)
Design iteration time: minutes - hours
Medium Fixed Cost (NRE)
  Still HW design
    More things to consider than SW
    Relatively slow design tools
Medium Incremental Cost
  FPGAs are general -> need larger die area to accommodate additional logic -> more cost/die
Good for lower volumes or when reconfigurability is required

## Slide 22: Questions

## Slide 23: ASICs vs FPGAs vs. Processors
Both FPGAs and Processors are ASICs. However, their applications are to be general deivices.
  Pros
    Flexible -> works for many needs
    Reconfigurable (In most cases) -> program or FPGA design can be changed
  Cons:
    not every user will need every component of the ASIC.

## Slide 24: Power and Delay in Transistors
Power for a Switching Event
  C is the capacitance of the load that the transistor is “driving”
    Typically transistors control other transistors. In CMOS, the input of the transistor being controlled looks like a capacitor.
  VDD is the positive voltage level supplied to the design
  f is the frequency of the switching event
Note how power scales with capacitance, voltage, and frequency
Delay
  The delay is related