## Slide 1: EECS151/251A Discussion 13
Christopher Yarp
May. 3, 2019

## Slide 2: Plan for Today
Hamming Code Practice
Faults
Questions

## Slide 3: Hamming Codes
Using the 7 bit Hamming code in lecture (4 data, 3 parity), encode 0010
Recall, in Hamming Codes, we start counting bit positions from 1, not 0
Parity bits are placed at bit positions that are powers of 2 (1, 2, 4, 8, …)
Bits in the group for parity bit contain all bit positions with a 1 in the nth most significant digit (counting from 1 as the LSb)
Parity bits are set such that the group has even parity
  If there is an even number of 1’s in a group (not including the parity bit) the parity bit for that group is set to 0
  If there is an odd number of 1’s in a group (not including the parity bit) the parity bit for that group is set to 1
The encoded word is: 0101010
1 | 2 | 3 | 4 | 5 | 6 | 7
001 | 010 | 011 | 100 | 101 | 110 | 111
P1 | P2 | D1 | P3 | D2 | D3 | D4
 | 1 | 2 | 3 | 4 | 5 | 6 | 7
 | 001 | 010 | 011 | 100 | 101 | 110 | 111
 | P1 | P2 | D1 | P3 | D2 | D3 | D4
P1 | Y |  | Y |  | Y |  | Y
P2 |  | Y | Y |  |  | Y | Y
P3 |  |  |  | Y | Y | Y | Y
1 | 2 | 3 | 4 | 5 | 6 | 7
001 | 010 | 011 | 100 | 101 | 110 | 111
0 | 1 | 0 | 1 | 0 | 1 | 0
Encoding Format:
Parity Bit Groups:
Parity Bit Groups:

## Slide 4: Hamming Codes
Decode 1010111 which was encoded with the 7 bit Hamming code in lecture (4 data, 3 parity).
The parity is computed for each group
  Group 1: C1 = P1+D1+D2+D4 = 1+1+1+1 = 0
    No error detected in group 1
    None of the bit’s in positions ??1 have an error
    P1, D1, D2, D4 are correct
  Group 2: C2 = P2+D1+D3+D4 = 0+1+1+1 = 1
    Error detected in group 1
    One of the bits in positions ?1? has an error
    P2, D1, D3, or D4 has an error
  Groups 3: C3 = P3+D2+D3+D4 = 0+1+1+1 = 1
    Error detected in group 3
    ne of the bits in positions 1?? has an error
    P3, D2, D3 or D4 has an error
C3 C2 C1 provides the position of the error
  The bit in position 110 has an error
  The decoded value us 1101
 | 1 | 2 | 3 | 4 | 5 | 6 | 7
 | 001 | 010 | 011 | 100 | 101 | 110 | 111
 | P1 | P2 | D1 | P3 | D2 | D3 | D4
P1 | Y |  | Y |  | Y |  | Y
P2 |  | Y | Y |  |  | Y | Y
P3 |  |  |  | Y | Y | Y | Y
1 | 2 | 3 | 4 | 5 | 6 | 7
001 | 010 | 011 | 100 | 101 | 110 | 111
1 | 0 | 1 | 0 | 1 | 1 | 1
1 | 2 | 3 | 4 | 5 | 6 | 7
001 | 010 | 011 | 100 | 101 | 110 | 111
1 | 0 | 1 | 0 | 1 | 0 | 1
Received:
Corrected:

## Slide 5: Hamming Codes
Implement a single error correcting Hamming code with 15 bits
If p is the number of parity bits and d is the number of data bits, the following relationship must be held: or
You were given that p+d = 15
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
 | 0001 | 0010 | 0011 | 0100 | 101 | 0110 | 0111 | 1000 | 1001 | 1010 | 1011 | 1100 | 1101 | 1110 | 1111
 | P1 | P2 | D1 | P3 | D2 | D3 | D4 | P4 | D5 | D6 | D7 | D8 | D9 | D10 | D11
P1 | Y |  | Y |  | Y |  | Y |  | Y |  | Y |  | Y |  | Y
P2 |  | Y | Y |  |  | Y | Y |  |  | Y | Y |  |  | Y | Y
P3 |  |  |  | Y | Y | Y | Y |  |  |  |  | Y | Y | Y | Y
P4 |  |  |  |  |  |  |  | Y | Y | Y | Y | Y | Y | Y | Y
,
Therefore, the 15 bit Hamming code contains 4 parity bits and 11 data bits
The rate of this code is 11/15 = 0.733
Compare this to the 7 bit code which had a rate of 4/7 = 0.571
Parity bits go into positions that are powers of 2

## Slide 6: Faults
Ideally, every device would behave exactly as we had envisioned it. However, the real world has other plans!

## Slide 7: Design Bugs (ex. logic bugs, timing closure bugs, power draw)
Timing bugs can be identified through timing analysis.
  Vivado and icc/Primetime do this for you and provide a timing report.
  The design is modified and the timing analysis is re-run until no timing errors exist
Power use can be estimated through power analysis
  Basis analysis assumes some average transistor activity
  More accurate analysis can be attained by capturing simulations of real workloads to derive realistic transistor activity factors
  Vivado and icc/PrimetimePx can do both of these for you
Logic bugs can be caught during the design phase through testing and formal methods
  Verilog testbenches which can be run in vcs, ModelSim, and Vivado Simulator
Checking that tools do not introduce bugs in your design
  Formal verification of the equivalence of 2 designs and simulation of theoretically equivalent systems are some common strategies
  Formality is a formal verification tool by Synopsys

## Slide 8: Manufacturing Defects
A lot can go wrong when producing an IC
  Wires can fuse
  Impurities can contaminate the product
  Process variations across runs, across shots of a mask, …
Attempts are made to limit these effects at the fab (factory)
  Limiting contamination by manufacturing in a Cleanroom with employees wearing special cleanroom attire
  Source heavily controlled materials and perform extensive incoming quality control
  Maintaining machines involved in production to high standards
  Modeling process variations and their effects
    Some models provided to IC designers
Photo Credit: Berkeley Marvell Nanofabrication Laboratory

## Slide 9: Manufacturing Defects
Fault and performance variations still occur despite our best efforts
Mitigated by testing dies for functionality and performance
  Sparing: use of extra on chip circuitry to account for faults
    Spare rows/columns in DRAM
    Disabling broken cores in multicore processors
  Binning: sorting dies based on performance
    High performance dies sold at a premium
A Bin Wafer Map:
Green = Bin 1 (Good Devices)
Image:
Y. A. Lin, "Parametric wafer map visualization," in IEEE Computer Graphics and Applications, vol. 19, no. 4, pp. 14-17, July-Aug. 1999. doi: 10.1109/38.773959

## Slide 10: Runtime Faults
Permanent Faults
  Caused by some irreversible physical damage
    Ex. Electromigration
Transient: temporary faults caused by the environment (ex. high energy particles)
  Tend to be randomly distributed across die
Intermittent: temporary faults that tend to occur repeatedly in the same place
    Possibly caused by a particular component operating sub-optimally in some situations
    Ex. unexpected delay change due to temperature change causing a timing failure
    May become permanent

## Slide 11: Runtime Faults – Do we need to worry about them?
“The critical limiters to long-term reliability in a high performance microprocessor are time-dependent dielectric breakdown (TDDB) and electromigration (EM) [4]–[6]. The TDDB is strongly dependent on voltage and moderately dependent on temperature…. On the other hand, EM is enormously dependent on temperature and strongly dependent on voltage…. The failure rate can vary many orders of magnitude over the typical range of operating conditions found in microprocessors for desktop and laptop systems.” [1]
[1] S. Sundaram et al., "Bristol Ridge: A 28-nm x86 Performance-Enhanced Microprocessor Through System Power Management," in IEEE Journal of Solid-State Circuits, vol. 52, no. 1, pp. 89-97, Jan. 2017. doi: 10.1109/JSSC.2016.2623637
[1]

## Slide 12: Runtime Faults – Do we need to worry about them?
Let’s talk about transient effects.
Many types of transient events are covered under the term Single-Event Effect (SEE).
  One particular type is the Single Event Upset (SEU) where the state of a storage element is changed
Caused by ionizing radiation [1]
  Cosmic rays [2]
  Alpha particles, particularly from packaging materials [2]
See [3] for an interesting slide deck
[1] https://www.intel.com/content/www/us/en/programmable/products/fpga/features/stx-single-event-upset.html
[2] https://www.intel.com/content/dam/www/programmable/us/en/pdfs/literature/wp/wp-01206-introduction-single-event-upsets.pdf
[3] https://indico.cern.ch/event/635099/contributions/2570672/attachments/1456364/2249943/Single_Event_Effecs_Radiation_Course_May_2017_SEE_CBP.pdf
Intel/Altera Rendering of a SEU [2]

## Slide 13: Runtime Faults – Do we need to worry about them?
Potential Negative Effects of SEU
  Changing the bit configuration in an FPGA
    Changes the programmed design
  Changing a pointer address in a program
  Changing a counter
  … you get the idea …
Mitigation Techniques:
  FPGA vendors are aware of SEUs employ have several mitigation techniques in their products [2]
    Include error correcting/checking and design methods that are SEU aware
  ECC Memory is used in servers and workstations
  Additional redundancy in safety critical and aerospace applications
Why do our consumer computers not crash constantly due to SEUs?
  They typically do not use ECC DRAM since it costs more
How much data stored in memory is critical?
There are typically a few important state elements and variables in a system.
If a bit flip occurs in a …
  Unused block of memory
  An image
  A text constant
  …
… it is unlikely that the SEU will crash the whole system.
[1] https://www.intel.com/content/www/us/en/programmable/products/fpga/features/stx-single-event-upset.html
[2] https://www.intel.com/content/dam/www/programmable/us/en/pdfs/literature/wp/wp-01206-introduction-single-event-upsets.pdf
[3] https://indico.cern.ch/event/635099/contributions/2570672/attachments/1456364/2249943/Single_Event_Effecs_Radiation_Course_May_2017_SEE_CBP.pdf