## Slide 1: EECS151/251A Discussion 3
Christopher Yarp
Feb. 8, 2019

## Slide 2: Latches

## Slide 3: Latches
There are several different flip-flop and latch types discussed in literature and the nomenclature can disagree at times.
In this class:
  a “flip-flop” is assumed to be a d flip-flop (edge triggered)
  a “latch” is assumed to be a device that passes a signal through when enabled (transparent) and holds the most recent value of its output when disabled (opaque)
They key difference between the flip-flop and latch is that the flip-flop only updates it’s output on a clock edge while the latch updates its output whenever its enable line is high and holds it otherwise

## Slide 4: Inferring Latches in Verilog
Latches can be inferred in Verilog by not assigning a reg type in all possible cases
In the case when the reg type was not assigned, Verilog assumes it’s value should remain unchanged
  This requires the previous value to be held …
  … which requires a latch

## Slide 5: Inferring Latches in Verilog
Combinational
module combo(input a, input b, input c, output reg d);
always @(*) begin
if(a) begin
d = b & c;
end else begin
d = b;
end
end
endmodule
endmodule
Latched (Sequential)
module latched(input a, input b, input c, output reg d);
always @(*) begin
if(a) begin
d = b & c;
end
end
endmodule
WARNING: [Synth 8-327] inferring latch for variable 'd_reg'

## Slide 6: Inferring Latches in Verilog
Assigning a reg type to itself in an always @(*) block also infers a latch
module self_loop(input a, input b, input c, output reg d);
always @(*) begin
if(a) begin
d = b & c;
end else begin
d = d;
end
end
endmodule

## Slide 7: Unintentional Latch Inference
Unintentional latch inference is one of the more common bugs you will probably come across
Especially when writing a big case statement or if/else tree (for example in an FSM), it can be easy to overlook assigning a reg type in all cases
Many synthesis tools will emit a warning if they infer a latch, look for these warnings and make sure any you see are intentional
  Vivado Synthesis Log: WARNING: [Synth 8-327] inferring latch for variable 'd_reg'

## Slide 8: Updating our understanding of always @ blocks
always @(*)
Describes a combinational circuit if reg types are assigned in all possible cases
Describes a sequential circuit (with latches) if reg types are not assigned in all cases
  Or are assigned to themselves
**Describes a sequential circuit (with latches) if not all signals are in the sensitivity list
  The synthesis tools may assume you meant to include the signal in the sensitivity list -> Vivado does
  Your simulator may not make the same assumption!
Always @(posedge clk)
Describes sequential circuits (with flip-flops)

## Slide 9: Blocking vs. Non-Blocking Assignment Conventions
… and why you should follow them

## Slide 10: Sequential Logic
Non-Blocking
always @(posedge clk)
begin
c <= a & b;
e <= c | d;
end
Blocking
always @(posedge clk)
begin
c = a & b;
e = c | d;
end
Are these the same module?
Notes: Move to discussion 2

## Slide 11: Sequential Logic
Non-Blocking
Blocking
Are these the same module? – No
Cycle | A | B | D | Non-Blocking | Blocking
0 | 0 | 1 | 0 | x | x
1 | 1 | 1 | 0 | x | 0
2 | 1 | 1 | 0 | 0 | 1
3 | 1 | 1 | 0 | 1 | 1
4 | 1 | 1 | 0 | 1 | 1

## Slide 12: Combinational Logic
Blocking
always @(a, b, d)
begin
c = a & b;
e = c | d;
end
Non-Blocking (Input Sensitivity)
always @(a, b, d)
begin
c <= a & b;
e <= c | d;
end
Non-Blocking (Intermediate Sensitivity)
always @(a, b, d, c)
begin
c <= a & b;
e <= c | d;
end
Are these the same module?

## Slide 13: Combinational Logic
Blocking
Non-Blocking (Input Sensitivity)
Non-Blocking (Intermediate Sensitivity)
Are these the same module? – ??
Cycle | A | B | D | Blocking | Non-Blocking (Input Sensitivity) | Non-Blocking (Intermediate Sensitivity)
0 | 0 | 1 | 0 | 0 | x | 0
1 | 1 | 1 | 0 | 1 | 0 | 1
2 | 1 | 1 | 0 | 1 | 0 | 1
3 | 1 | 1 | 0 | 1 | 0 | 1
WARNING: [Synth 8-567] referenced signal 'c' should be on the sensitivity list [/home/cyarp/test_blocking/combinational_nonblocking_input_only.v:33]
Looks like a latch. Where is it??

## Slide 14: Keep to the Rules of Thumb
Sequential Logic: Use non-blocking assignments
Combinational Logic: Use blocking assignments
You can always break up your sequential logic into combinational and sequential components
  Allows you to cleanly have intermediates in your combinational logic
always @(*)
begin
c = a & b;
next_state = c | state;
end
always @(posedge clk)
begin
state <= next_state;
end
D
Q
clk
Comb. Logic
Comb. Logic

## Slide 15: Implementing Logic Functions with LUTs

## Slide 16: LUT
LUT is short for “Look Up Table”
The number of rows in the table is 2N where N = number of input bits
There is 1 row for every possible input combination
  If you view the inputs as a single multiple bit wide wire, you can think of it as specifying an address in the LUT
The designer determines what the output will be for each row of the table

## Slide 17: Implementing Functions with LUTs
You can view the entries of an N-input LUT as being entries in a truth table for an N-input combinational logic block
Since the LUT contains a row for every possible combination of inputs, we can implement any combination function by specifying the output values for each row in the table

## Slide 18: What function is this?
This LUT only outputs 1 when A, B, and C are all true.
This LUT is implementing A&B&C
{C,B,A} | C | B | A | Out
0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0
2 | 0 | 1 | 0 | 0
3 | 0 | 1 | 1 | 0
4 | 1 | 0 | 0 | 0
5 | 1 | 0 | 1 | 0
6 | 1 | 1 | 0 | 0
7 | 1 | 1 | 1 | 1

## Slide 19: What function is this?
This outputs 1 only when exactly 1 of A, B, and C are true
A&(~B)&(~C) | (~A)&B&(~C) | (~A)&(~B)&C
{C,B,A} | C | B | A | Out
0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 1
2 | 0 | 1 | 0 | 1
3 | 0 | 1 | 1 | 0
4 | 1 | 0 | 0 | 1
5 | 1 | 0 | 1 | 0
7 | 1 | 1 | 0 | 0
7 | 1 | 1 | 1 | 0

## Slide 20: Implementing Functions with LUTs
If you can write a truth table for it (which you can with any combinational block), you can implement it with a single LUT!
This does not necessarily mean you should implement all combinational functions with a single LUT:
  A combinational block with 64 inputs would require a LUT of 264 ≅ 1.84x1019 entries! Just storing all of the output bits would require 2305843 TB of data!
    When would you want a 64 input combinational block? How about a 32 bit adder (32 bits for each input operand)
  There is likely a more efficient way of implementing a 64 input combinational block

## Slide 21: Building Larger LUTs
… with smaller LUTs

## Slide 22: Building Larger LUTs
d | c | b | a | out
0 | 0 | 0 | 0 | o1
0 | 0 | 0 | 1 | o2
0 | 0 | 1 | 0 | o3
0 | 0 | 1 | 1 | o4
0 | 1 | 0 | 0 | o5
0 | 1 | 0 | 1 | o6
0 | 1 | 1 | 0 | o7
0 | 1 | 1 | 1 | o8
1 | 0 | 0 | 0 | o9
1 | 0 | 0 | 1 | o10
1 | 0 | 1 | 0 | o11
1 | 0 | 1 | 1 | o12
1 | 1 | 0 | 0 | o13
1 | 1 | 0 | 1 | o14
1 | 1 | 1 | 0 | o15
1 | 1 | 1 | 1 | o16
Let’s say we have 3 input LUTs, is there a way we could create a 4 input LUT?
Yes, let’s look at the truth table for a 4 input LUT
The bottom half of the table looks like a repeat of the top half of the table except …
  The top half of the table is when d is 0, the bottom half is when d is 1
  The top and bottom halves of the table have different outputs
d | c | b | a | out
0 | 0 | 0 | 0 | o1
0 | 0 | 0 | 1 | o2
0 | 0 | 1 | 0 | o3
0 | 0 | 1 | 1 | o4
0 | 1 | 0 | 0 | o5
0 | 1 | 0 | 1 | o6
0 | 1 | 1 | 0 | o7
0 | 1 | 1 | 1 | o8
1 | 0 | 0 | 0 | o9
1 | 0 | 0 | 1 | o10
1 | 0 | 1 | 0 | o11
1 | 0 | 1 | 1 | o12
1 | 1 | 0 | 0 | o13
1 | 1 | 0 | 1 | o14
1 | 1 | 1 | 0 | o15
1 | 1 | 1 | 1 | o16
d | c | b | a | out
0 | 0 | 0 | 0 | o1
0 | 0 | 0 | 1 | o2
0 | 0 | 1 | 0 | o3
0 | 0 | 1 | 1 | o4
0 | 1 | 0 | 0 | o5
0 | 1 | 0 | 1 | o6
0 | 1 | 1 | 0 | o7
0 | 1 | 1 | 1 | o8
1 | 0 | 0 | 0 | o9
1 | 0 | 0 | 1 | o10
1 | 0 | 1 | 0 | o11
1 | 0 | 1 | 1 | o12
1 | 1 | 0 | 0 | o13
1 | 1 | 0 | 1 | o14
1 | 1 | 1 | 0 | o15
1 | 1 | 1 | 1 | o16

## Slide 23: Let’s split the table
d | c | b | a | out
0 | 0 | 0 | 0 | o1
0 | 0 | 0 | 1 | o2
0 | 0 | 1 | 0 | o3
0 | 0 | 1 | 1 | o4
0 | 1 | 0 | 0 | o5
0 | 1 | 0 | 1 | o6
0 | 1 | 1 | 0 | o7
0 | 1 | 1 | 1 | o8
1 | 0 | 0 | 0 | o9
1 | 0 | 0 | 1 | o10
1 | 0 | 1 | 0 | o11
1 | 0 | 1 | 1 | o12
1 | 1 | 0 | 0 | o13
1 | 1 | 0 | 1 | o14
1 | 1 | 1 | 0 | o15
1 | 1 | 1 | 1 | o16
c | b | a | out
0 | 0 | 0 | o1
0 | 0 | 1 | o2
0 | 1 | 0 | o3
0 | 1 | 1 | o4
1 | 0 | 0 | o5
1 | 0 | 1 | o6
1 | 1 | 0 | o7
1 | 1 | 1 | o8
c | b | a | out
0 | 0 | 0 | o9
0 | 0 | 1 | o10
0 | 1 | 0 | o11
0 | 1 | 1 | o12
1 | 0 | 0 | o13
1 | 0 | 1 | o14
1 | 1 | 0 | o15
1 | 1 | 1 | o16
When d is 0:
When d is 1:
Notes: Note: Same set of inputs to each of the 2 tables. However, different outputs

## Slide 24: Select which table to use
c | b | a | out
0 | 0 | 0 | o1
0 | 0 | 1 | o2
0 | 1 | 0 | o3
0 | 1 | 1 | o4
1 | 0 | 0 | o5
1 | 0 | 1 | o6
1 | 1 | 0 | o7
1 | 1 | 1 | o8
c | b | a | out
0 | 0 | 0 | o9
0 | 0 | 1 | o10
0 | 1 | 0 | o11
0 | 1 | 1 | o12
1 | 0 | 0 | o13
1 | 0 | 1 | o14
1 | 1 | 0 | o15
1 | 1 | 1 | o16
When d is 0:
When d is 1:
a
b
c
d
out

## Slide 25: Simulation

## Slide 26: Initial blocks
Initial blocks are executed at the start of the simulation
  In general, initial blocks are not synthesized
You can have multiple initial blocks in the same module
  Each will run in parallel starting at the beginning of the simulation
initial begin
$dumpfile("dump.vcd");
$dumpvars;
a = 1;
#4
a = 0;
#10
$finish();
end
initial begin
#1
forever begin
$strobe("time: %4d, a: %b, b: %b, c: %b", $time, a, b, c);
#2;
end
end

## Slide 27: Forever blocks
Will execute a sequence of Verilog statements repeatedly forever (until the simulation ends)
initial begin
#1; //Wait 1 Cycle
forever begin //Print out values every 2 cycles
$strobe("time: %4d, a: %b, b: %b", $time, a, b);
#2;
end
end

## Slide 28: Waiting for Events
So far, we have used the delay statement, #
If we want to wait for a particular even to happen, we can use another type of statement: @(posedge signal) or @(negedge signal)
initial begin
$dumpfile("dump.vcd");
$dumpvars;
a = 1;
@(negedge clk) //Continue simulation until the next negative edge of clk
a = 0;
@(negedge clk) //Continue simulation until the next negative edge of clk
#4 //Continue for 4 periods
$finish();
end

## Slide 29: Repeat blocks
You may want to repeat a block of Verilog a fixed number of times
Repeat blocks let you do that
repeat (10) begin //Repeat this 10 times
  signal = ~glitchy_signal;
  @(negedge clk);
end

## Slide 30: And even more …
There are other loop statements in Verilog
  For loops
  While loops
  Note that these are different from generate loops
You can also fork multiple parallel threads of execution in an initial block, wait for all of them to finish, then continue executing Verilog expressions
  These are called fork-join blocks
  Having multiple initial blocks is also a way to create multiple parallel threads of execution that all start when the simulation starts