## Slide 1: EECS151/251A Discussion 5
Christopher Yarp
Feb. 21, 2019

## Slide 2: Plan for Today
FSM Practice
Ready/Valid Interfaces
Transistor Level Logic Implementation
  Logic with Mux & Pass Gates

## Slide 3: FSM Practice

## Slide 4: Designing a Door Controller for Cory 125
﻿The door is normally locked
Any Cal1Card will unlock the door for 10 seconds.
  The card reader will not respond to another card during that time.
Cory 125 has a motion detector on the inside of the door. When motion is detected, the door may be opened from the inside for up to 30 seconds without sounding the alarm.
  Any use of a Cal1Card during this time should unlock the door for the appropriate amount of time.
  The alarm should not go off while the door is unlocked.
  The alarm may still be disabled by the motion detector after the door is locked again.
  Any activation of the motion detector while the alarm is disabled will delay the re-arming of the alarm until 30 seconds later.
If the door is opened without the motion detector being triggered or a Cal1Card being used, the alarm sounds.
  The door can be returned to normal with the lab manager’s Cal1Card (ID = 0001).
  All entry into Cory 125 is disabled when the alarm is sounding.
Timers for 10 and 30 seconds are provided
  Both have a start input which resets and starts the counter when asserted
  Both timers have a ”done” signal which will be brought high for 1 cycle when the timer expires

## Slide 5: Designing a Door Controller for Cory 125
Despite what seems like a simple job, the state machine for this problem can get complex
  Mostly because of special cases we need to consider
We’ll make this manageable by looking at each state, one at a time

## Slide 13: Observations about this FSM
Mealy vs. Moore
  We designed a Mealy style FSM for the door controller
  Would we need any extra states to formulate it as a Moore machine?
    How about all those times we restarted timers?
If we had information on whether or not timers were running, we probably could have eliminated the “Unlocked & Motion Detected” state
  Would have required changing/adding arcs to the FSM

## Slide 14: Ready/Valid Interfaces

## Slide 15: Interfacing Between Modules & Ready/Valid
Up to this point, we have been primarily using modules that we have written ourselves.
  We know how the control logic for our modules works and how to interface with it
What if we want to integrate with modules written by others, without knowing all the specifics of their control logic?
Standard interfaces, such as ready/valid, help us do this

## Slide 16: Semantics of Ready/Valid Transfer
The producer (source, master) is sending data to the consumer (sink, slave)
The data to be transferred is placed on the ‘data’ line
Valid = 1 indicates that the values on the ‘data’ line are valid
Ready = 1 indicates that the consumer is ready to consume ‘data’ on the next posedge of the clock
A transfer occurs at the positive edge of the clock when ready and valid are both high

## Slide 17: Semantics of Ready/Valid Transfer

## Slide 18: Semantics behind Ready/Valid Use
What are the responsibilities for the producing and consuming modules?
  When should producer required to pull the valid line high?
    Should the producer wait for the ready line to go high before pulling valid?
  When should the consumer pull the ready line high?
    Should the consumer wait for valid data to be present before pulling ready?
Module writers taking opposing assumptions can result in deadlock
  Producer is waiting for consumer to become ready before raising valid high
  Consumer is waiting for the producer to present valid data before becoming ready
  Nothing will ever happen! They will wait for each other forever!

## Slide 19: AXI4-Stream Ready/Valid Semantics
AXI4 Streaming is a Ready/Valid style interface standard which answers the question of what the producer and consumer are responsible for
Standard developed by ARM as part of the AMBA Series of Standards
  A common bus standard used in SoC and FPGA projects
Most signal names have a ‘t’ prepended to them
  tvalid, tdata, tready
Signal clock is called aclk
Reset is called aresetn (active low)
Contains additional optional control lines
  ex. tlast denotes the last word transferred in a packet
Full specification available at: http://infocenter.arm.com/help/index.jsp?topic=/com.arm.doc.ihi0051a/index.html (requires registration with ARM)

## Slide 20: AXI4-Stream Ready/Valid Semantics Summary
Transfer occurs when both valid and ready are asserted (at a positive clock edge)
Producer:
  The producer is cannot to wait for ready to be high before asserting valid
    The producer must assert valid when possible
  The producer must hold valid high and data constant until transaction occurs
Consumer:
  The consumer may wait for valid to be true before asserting ready
    This can waist a clock cycle
  The consumer may assert ready when no valid data is present
    This is the best option for most consumers as transactions will occur on the next clk rising edge
  The consumer is allowed to de-assert ready (if ready was already asserted) before valid is asserted

## Slide 21: Implementing Logic With Pass Gates

## Slide 22: Implementing Logic with Pass Gates

## Slide 23: Implementing Logic with Pass Gates