## Slide 1: EECS151/251A Discussion 9
Christopher Yarp
Apr. 5, 2019

## Slide 2: Plan for Today
Practice Problem
Processor Review
Your Questions

## Slide 3: Recall Different Memory Memory Technologies
6T SRAM: Crossed coupled inverters (4 transistors) + 2 access transistors
1T DRAM: Data stored in capacitor. 1 transistor to write and read value. Read is a destructive operation
3T DRAM: Data is stored in transistor capacitance. 2 transistors to read, 1 to write. Read is non-destructive.

## Slide 4: Memory Technology Practice Problem
A device requires a 2 MiB (1MiB = 1024*1024 bytes) cache
The cache line is 32 32-bit words
The silicon foundry you are using includes 6T SRAM cells and 3T DRAM cells in the design kit for the CMOS logic process you are planning to use to implement your processor.
You want to have an equal number of rows and columns in the memory. How many rows and columns do you need?
What is the approximate size difference between an SRAM version of the memory and the DRAM version of the memory (assume all transistors are the same size and ignore the periphery logic).
What are some of the principle disadvantages of the DRAM cell compared to the SRAM cell?
Why do you suspect the silicon foundry did not provide a 1T DRAM cell for this CMOS logic process?

## Slide 5: Number of Rows & Columns
We want an equal number of rows and columns if possible.
The number of bits in the memory is 2 MiB = 2*1024*1024*8 = 1024^2 * 4^2.
The number of columns & rows is ideally sqrt(1024^2 * 4^2) = 4096
The cache lines are 32*32 = 1024 bits wide
1024 fits evenly into 4096: 4096 is an acceptable number of columns
Rows: 4096
Columns: 4096

## Slide 6: Area Comparison
The 3T DRAM requires 3 transistors
The 6T SRAM requires 6 transistors
If we neglect the size of the transistors and the difference in wiring, the 3T DRAM cell is approximately ½ the size of the 6T SRAM cell
This would lead to an array that is approximately ½ the size
Note: this is a back of the envelope approximation. SRAM and DRAM are wired differently which will have impacts on the size of the cells and the periphery logic.
However, DRAM can generally be more dense than SRAM

## Slide 7: Disadvantages of 3T DRAM
Even through the 3T DRAM does not have destructive read operations (like 1T DRAM), leakage still exists.
Charge will slowly leak off the capacitor, requiring values to be periodically refreshed.
DRAM is also non-restoring while SRAM is restoring
  Makes DRAM more sensitive to noise and other non-idealities

## Slide 8: Why is the 1T DRAM Unavailable?
1T DRAM requires larger capacitance in the cell than what can be provided in a digital logic focused process.
Special DRAM processes exist which allow large capacitors to be formed.
These processes are typically not as well optimized for digital logic. This is why we don’t typically use DRAM processes when implementing logic heavy ASICs.
The integration of DRAM with logic is an ongoing research topic with 3D stacking of DRAM dies on top of CMOS dies being one option
  Lookup HBM (High Bandwidth Memory) if you are interested

## Slide 9: Quick Review – Single Cycle RISCV

## Slide 10: The 5 Stage Pipeline
In general, most RISC Load/Store style processors need to accomplish 5 tasks when executing an instruction. Each task can be made into a separate pipeline stage (the 5 stage pipeline).
  IF (Instruction Fetch): Fetch the Instruction from Memory
  ID (Instruction Decode): Decode what the instruction does, set control signals for the instruction, fetch relevant values from the register file
  EX or X (Execute): Execute the instruction if it is an arithmetic instruction (using the ALU). Compute addresses for memory load/store commands. Determine if a branch is taken or not.
  MEM or M: Read from memory if the instruction is a load, write to memory if the instruction is a store
  WB (Write Back, or Register Write): Write the value computed by the ALU (for arithmetic instructions) or a value read from memory (load instructions) into the register file.
In the labs and in the HW, we ask for a 3 stage pipeline. Some of these functions need to me merged together

## Slide 11: Pipelining for Speed
Note the control signals are pipelined
rd address is also pipelined

## Slide 12: Pipelining for Speed
Notes: Components in each pipeline stage are shown in a different color

## Slide 13: Data Hazard
sub r5, r3, r4
add r3, r1, r2
Data Hazard
The result of the add instruction will not be in the reg file when the sub instruction tries to read it
Notes: Components in each pipeline stage are shown in a different color

## Slide 14: Data Hazards & Load Hazards
2 Main Options for Dealing with Data Hazards
  Stalling: Stall the other pipeline stages of the processor while you wait for an another instruction to finish
    Involves freezing the program counter and preventing new instructions from being written into pipeline registers
  Forwarding: Send the required information back to an earlier pipeline stage (in parallel with it being written into the register file)
Load hazards are similar to Data Hazards: the value read from memory will not be ready for the

## Slide 15: ALU Forwarding

## Slide 16: Why don’t we forward memory loads too?

## Slide 17: Forwarding memory results in a long critical path

## Slide 18: Control Hazards
We usually expect that the next instruction to be executed will be the next instruction in the program (PC+4).
There are 2 main cases when this is not true:
  Jump instructions: execution jumps to a specified instruction unconditionally
  Branch instruction: execution jumps to a specified instruction if a condition is satisfied
Where does the hazard come from?
  In a pipelined processor, you may not know that an instruction is a jump or branch until another instruction has already entered the pipeline
    You you may need to wait additional cycles for it to be determined if a branch is taken or to compute a target address
How do we resolve the hazard?
  We turn the instruction we fetched in error into a NOP (no operation) instruction
    The most important thing is that this instruction should not modify any state (including the PC)
  The NOP runs through the pipeline like any other instruction.

## Slide 19: Tips for Implementing Processors
Diagramming is a very important step in the design process
  It helps you think through the major design decisions before getting lost in Verilog
While it is easy to focus on the datapath of the processor, it is important to not neglect the control signals
A common source of bugs in processor implementations in the lab come from the control logic
Keep careful track of:
  What control signals are needed?
  When are they needed?
  What information is required to correctly make control decisions?
  Where/when does this information come from (the same or different pipeline stage)?
  Is all the information available to make a decision?
    Is a stall required?
    Was a prediction made which needs to be validated or invalidated?